## Slide 1
Fluid dynamics

## Slide 2
A microscopic view
Gas
Fluid
compressible
Liquid
Fluid
Incompressible
Solid
rigid body

## Slide 3
What new physics is involved?
Fluids can flow from place-to-place
Their density can change if they are compressible (for example, gasses)
Fluids are pushed around by pressure forces
An object immersed in a fluid experiences buoyancy

## Slide 4
Density
The density of a fluid is the concentration of mass
Mass = 100 g = 0.1 kg
Volume = 100 cm3 = 10-4 m3
Density = 1 g/cm3 = 1000 kg m3

## Slide 5
Pressure
Pressure is the concentration of a force – the force exerted per unit area
Greater pressure!
(same force, less area)
Exerts a pressure on the
sides and through the fluid

## Slide 6
Pressure
Units of pressure are N/m2 or Pascals (Pa) – 1 N/m2 = 1 Pa
Atmospheric pressure = 1 atm = 101.3 kPa = 1 x 105 N/m2

## Slide 7
Gauge Pressure
Gauge Pressure is the pressure difference from atmosphere. (e.g. Tyres)
Notes: Do by hand.

## Slide 8
Fluid Dynamics
Laminar (steady) flow is where each particle in the fluid moves along a smooth path, and the paths do not cross.
Turbulent flow above a critical speed, the paths become irregular, with whirlpools and paths crossing. Chaotic and not considered here.
Streamlines spacing measures velocity and the flow is always tangential, for steady flow don’t cross. A set of streamlines act as a pipe for an incompressible fluid
Non-viscous flow – no internal friction (water OK, honey not)

## Slide 9
Conservation of Mass: The Continuity Eqn.
The rate a fluid enters a pipe must equal the rate the fluid leaves the pipe. i.e. There can be no sources or sinks of fluid.
“The water all has to go somewhere”

## Slide 10
Conservation of Mass: The Continuity Eqn.
v1
v2
A1
A2
Q. How much fluid flows across each area in a time :
fluid in 
fluid out 
v1Dt
A1
v2Dt
A2

## Slide 11
Conservation of Energy: Bernoulli’s Eqn.
v2Dt
v1Dt
What happens to the energy density of the fluid if I raise the ends ?
Energy per unit volume
y1
y2
Total energy per unit volume is constant at any point in fluid.

## Slide 12
Summary: fluid dynamics
Continuity equation: mass is conserved!
For liquids:
Bernoulli’s equation: energy is conserved!