## Slide 1
heat

## Slide 2
Temperature
Temperature is a measure of the average kinetic energy of the individual particles in a substance.

## Slide 3
Temperature Scale

## Slide 4
The Zeroth Law of Thermodynamics
If bodies A and B are each in thermal equilibrium with a third body C, then A, B, and C are in thermal equilibrium with each other.
Every body has a property called temperature. When two bodies are in thermal equilibrium, their temperatures are equal. And vice versa.

## Slide 5
Temperature and Heat

## Slide 6
Heat
Heat is defined as the transfer of energy across the boundary of a system due to a temperature difference between the system and its surroundings.
Units of Heat
The calorie (cal), which is defined as the amount of energy transfer necessary to raise the temperature of 1 g of water from 14.5°C to 15.5°C
British thermal unit (Btu), which is defined as the amount of energy transfer required to raise the temperature of 1 lb of water from 63°F to 64°F.

## Slide 7
The heat capacity C of a particular sample of a substance is defined as the amount of energy needed to raise the temperature of that sample by 1°C.
Heat Capacity and Specific Heat
The specific heat c of a substance is the heat capacity per unit mass. Thus, if energy Q transferred by heat to mass m of a substance changes the temperature of
the sample by T, then the specific heat of the substance is

## Slide 8
Specific
Heat

## Slide 9
Conservation of Energy

## Slide 10
Laten Heat

## Slide 11
Laten Heat

## Slide 12
Heat Transfer Mechanism

## Slide 13
k = thermal conductivity (W/m.K) ε = emissivity
h = heat transfer coefficient (W/m2.K) cp = specific heat (J/kg.K)
σ = The Stefan-Boltzmann Constant = 5.6703 x 10-8 (W/m2K4)
Heat Transfer Mechanism