## Slide 1: METHODS OF GRAIN DRYING
4Th Group from AGT B
Ari Suryaningsih 201412024
Deka Delta Lita 2014121028
Sadam Husein Abdullah Elkatiri 2014121026

## Slide 2: Table of contents HEATED AIR DRYING 01 02 03 04 RADIATION DRYING SUN DRYING INFRARED DRYING

## Slide 3: Table of contents (pt. ii) SOLAR DRYING INTEGRATED HYBRID-TYPE SOLAR GRAIN DRYER CHEMICAL DRYING SACK PRyING DIELECTIC AND MICROWAVE DRYING

## Slide 4: 1. Heated air drying
Advantages
Independent of weather
Fast drying
High drying capacity per fan horsepower

## Slide 5: 1. Heated air drying
Disadvantages
Higher initial investment and maintenance cost
Considerable fuel expenditure
Danger of fire hazard
Requires skilled man power for control of drying condition
By direct firing with liquid fuel, products contaminated with flue gases

## Slide 6: 2. Radiation draying
Based on the absorption of radiant energy of the sun and its transformation into heat energy by the grain. Ex: sun drying
Accomplished with the acid of special infrared radiation generators, infrared lamp

## Slide 7: 3. Sun drying
Advantages
- No fuel or mechanical energy is required
- Operating is very simple
- Viability, germination, baking qualities are fully preserved
- Microbial activity and insect/pest infestation are reduced
Labor-oriented
-No pollution

## Slide 8: 3. Sun drying
Disadvantages
Completely dependent on wheather
Not possible round the clock or round the year
Excessive losses occur due to shattering, birds, rodents
Requires specially constructed large floor area, restricting the capasity of mill to a certain limit
The entire process id unhygienic
Unsuitable for handling of large quantity of grain within a short

## Slide 9: 4. Infrared drying
Infrared rays can penetrate into the irradiated body to a certain depth and transform into heat energy. Special infrared lamps, or metalic and ceramic surface heated to a specified temperature by an open flame, may be used as generators of infrared radiation.
Advantages
Small thermal inertia
Simplycity and safety in operation of lamp radiation dryers
Disadvantages
High expenditure of electric power
Low utilization factor
Radiation dryers have been used in many countries for drying the painted surfaces of machinery, and in timber processing, textile industry, and cereal grain and other food industries.

## Slide 10: 5. Solar drying
A solar drying system can be effectivenly utilized in tropical and subtropical countries where solar energy is abundantly available and solar insolation is also appreciably high. Various designs and capacities of solar dryers with the variations in efficiency are available.
One of the major components of a solar dryer is an absorber that receives and absorbs solar spectrum of radiation. This absorber transforms the radiation energy to thermal energy for heating air flowing over it, which can be utilized as a drying medium. Solar air dryers can be classified into mode or indirect mode.
Natural convection solar dryers do not require any fan or blower for air circulation in the dryers. Hence, these dryers are cheap and easy to operate. but, the drying operation wwould be slow and take longer drying time. The simple solar cabinet dryers comee under this category.
In the category of forced convection solar dryers, blowers circulate adequate quantitty of the air through the drying material. These dryers cart dry a comparatively large quantity of material with a reduced drying time. Bin type-forced convection solar dryers are quite common.9

## Slide 11: 6. Intergrated hybrid-type solar grain dryer
Solar energy is not available round the clock and the year round. Hence, an auxiliary air-heating system in necessary for a continuous drying operation. An improved solar energy storege system may not be economical. In view of these common problems, a solar-cum-husk-fired flue gas grain drying system of 1 ton/day capacity has been patented by Chaktaverty, DAS, an IIT, Kharagpur, India, for commercial exploration. It compriese an inclined roof cum solar flat plate collectpr for heating air, a husk-fired furnance, and a grain dryer. It is suitable for drying grain grain for both seed and food purposes. Its principle, structure, and operations are detailed in Chakraverty et al. (1987).

## Slide 12: 7. Dielectric and Microwave drying
In dielectric drying heat is generated within the solid by placing it in a fixed high frequency current. The molecules of the substance, placed in a field of high frequency current are polarized and begin to oscillate in accordance with the frequency. The main advantage of this method is that the substance is heated with extraordinary rapidity.
The dielectric drying has now been in use in different industries such as timber, plastics, and cereal grain processing.

## Slide 13: 8. Chemical Drying
Various chemicals such as sodium chloride, calcium propionate, copper sulfate, ferrous sulfate, urea, etc., have been tried for preservation of wet paddy. Of these, common salt has been proved to be effective and convenient for arresting deteriora tive changes during storage.
Advantages:
It not only dries paddy but also reduces the damage due to fungal, microbial. and enzymatic activities and heat of respiration
It does not affect the viability of the grain.
The milling quality of paddy is satisfactory
Loss of dry matter is negligible
It does not affect the quality of rice bran.

## Slide 14: 8. Chemical Drying
Disadvantages:
The moisture may be retained on the husk due to the presence of sodium chloride
The useful life of gunny will be shortened
The color of hush changes to dark yellow.
The common sali-treated paddy requires an additional drying subsequently
Economy of the process has yet to be established.

## Slide 15: 9. SACK PRYING
This method is particularly suitable for drying of small quantities of seed to prevent mixing of varieties and conserve strain purity and viability. The grain bags are laid flat over holes cut on the floor of a tunnel system so thatheated air can be forced up through the grain from an air chamber underneath. Usually an air temperature of 45°C with an airflow rate of 4 m/min at 3-4 cm static pressure per hag of 60 kg is used for fastest drying rate. The sacks are turned once during the drying operation. The sack drying process involves higher labor cost.

## Slide 16: THAT IS ALL & tHANKYOUU